ASMOTOM  ATS

- Automated Trephine System for perforating keratoplasty

- Trephination of Patient and Donor eyes as well as corneo-scleral discs with separate instrumentation sets

- Cutting depth pre-adjustable for the patient

- Cutter sets for five different diameters included

ASMOTOM ATS – a revolutionary automated trephine system to aid corneal transplantation

The ASMOTOM ATS uses an innovative double fixation design. Vacuum is applied to both, the central and the peripheral section of the cornea.

A new feature allows the cutting depth to be pre-set using offset rings.

The trephine rotates between the two concentric areas of fixation, using an automatic feed. Once the pre-set depth is reached, the cutter retracts back into its initial position, holding on to the separated central portion, until vacuum is released.

#### Advantages of the ASMOTOM System

- Easy centering using the new ASMOTOM Marker

- Pre-adjustment possibility for cutting depth

- Double suction principle provides secure fixation

- Precise cutter feed produces perfectly straight edges, accelerating the healing process and reducing induced astigmatism, which lead to better post operative results

- Elimination of the need to apply pressure to the cornea during trephination reduces the chance of iris damage

- Anterior chamber maintainer not required for transplant trephination, reducing handling of the transplant

- Separate, color coded hand piece sets for patient and donor

- Gentle on endothelial cells, due to effortless penetration

- Both hand piece sets include two trephines for each of five different diameters from 6,0 to 8,2 mm

- Patient and donor cutter sizes are paired for transplant fit

- Both hand piece sets are stored on their own, organized sterilizing tray, contained in a common sterilizing case, which serves for storage and sterilization.

Distributed by GENERAL INNOVATIONS

##### 7334 Hollister Avenue Suite i

##### Goleta, CA  93117 USA

Phone: +1 (805) 685-9991 Fax:  +1 (805) 685-1292

Visit us at:  WWW.generaltrade.net, or E-mail us to:  gimsg@earthlink.net

# Text boxes

ASMOTOM Marker

Control unit, footswitch, and hand pieces for patient and donor

The ASMOTOM ATS produces beautiful straight edges

Completely assembled Patient hand piece

Organized cases for the sterilization and safe storage of patient and donor hand piece sets